## Slide 1
IT4010 Research Project – 2026 Jan
AI-Assisted IoT Disaster Monitoring
& Emergency Response System
Floods · Landslides · Cyclone Impacts | Sri Lanka
Project ID: R26-IT-146
Research Group: AIMS – Autonomous Intelligent Machines & Systems
Specialization: Information Technology (IT)
Supervisor: Dr. Kapila Dissanayake
Team: IT22557506 · IT22272386 · IT22638168 · IT22284716

## Slide 2
1 & 2 — Abstract & Problem Background
Abstract
This project builds a low-cost, explainable, and demonstrable prototype for disaster monitoring & emergency response focused on Floods, Landslides, and Cyclone impacts in Sri Lanka. It integrates low-cost IoT sensor nodes (rainfall, water level, soil moisture), weather forecasts, and crowdsourced citizen reports. A central server runs simple, explainable decision logic (rule-based + lightweight classifiers) and a scoring engine to compute per-area impact scores, maps those scores to risk levels (Low/Medium/High), and dispatches geofenced alerts to citizens and authorities via a mobile/web app and dashboard. The emphasis is on practical feasibility, explainability, and a complete end-to-end demo.
Problem Background
1
Sri Lanka experiences frequent monsoon and cyclone-driven events causing floods, landslides, and infrastructure failures.
2
Existing national meteorological & hydrological systems provide accurate large-scale forecasting but are sparse for localized, ground-level conditions.
3
When communications fail, authorities lack up-to-date situational awareness — rescue teams cannot quickly identify where to go.
4
There is a need for a low-cost, local sensing + explainable decision support system to provide timely, actionable alerts for citizens and responders.
References: UNDRR Global Assessment (2022), WMO guidelines (2018)

## Slide 3
3 — Project Goal, Objectives & Scope
Main Goal:
Build a demonstrable, low-cost AI-assisted IoT system to detect and notify about flood, landslide, and cyclone impacts at a local (village/ward) scale to improve situational awareness and rescue coordination.
Objectives
O1
IoT Node
Implement at least one ESP32 IoT node measuring rainfall, water level and soil moisture.
O2
Server
Implement a server that ingests sensor, weather and crowdsourced data.
O3
AI Logic
Implement explainable decision logic to classify risk (Low / Medium / High).
O4
App & Dashboard
Citizen-facing app to receive alerts and submit reports + authority dashboard for monitoring/response.
O5
Validate & Demo
Validate system with simulated and available historical data; demonstrate an end-to-end scenario.
Scope
• Prototype-level: IoT nodes
• Local server or free cloud
• Simple mobile/web frontend & dashboard
• Cyclone handling is impact-based (NOT forecasting)

## Slide 4
4 — Key Contributions / Novelty
📡
Low-Cost Multi-Parameter IoT Node
Single ESP32 node measures rainfall, water level, and soil moisture — supports flood, landslide and cyclone-impact inference without expensive wind sensors. Cost < $15–25 per node.
🧮
Explainable Impact Scoring Engine
Transparent weighted formula combining weather forecasts (Rf, Wf, Pt), local sensor readings (Sr, Sw, Ss), and report credibility (Rc) × vulnerability factor V. Every intermediate value is logged.
📷
Multi-Modal Validation (Image + Sensor)
Image-based crowdsourced report verification fused with sensor corroboration to reduce false alarms. CNN classifies severity (0=dry, 1=shallow, 2=deep); result cross-validated with nearest sensor reading.
📍
Geofenced Targeted Alerts
Region partitioned into polygons (wards/1km² tiles). Alert dispatched only to users whose last GPS falls within a polygon whose impact score exceeds threshold. Minimizes alert fatigue for unaffected populations.
References: Silva et al. (2020); NOAA/WMO impact-based warnings guidance

## Slide 5
5 — High-Level Architecture
1
IoT Sensor Nodes
(ESP32)
rain · water level · soil moisture
every 5–15 min
→
2
Message Broker
/ Ingest API
HTTP POST or MQTT
/ingest/sensor
→
3
Server:
Preprocess & DB
filter noise · deltas
MongoDB / Firebase
→
4
AI / Decision
Layer
rule-based + classifier
scoring engine
→
5
Alert Dispatcher
geofence → FCM push
admin dashboard
Weather API → Server
Citizen App → Server (reports, SOS)
User App
(Citizens)
Authorities
Dashboard
Logs &
Export
Key flow: sensors + weather + reports → preprocess → decision/score → geofenced alerts → dashboard
Reference: Project doc Fig 1.0

## Slide 6
6 — Components & Data Flow (Detailed)
IoT Sensor Node
• ESP32 reads sensors → packages JSON → sends to /ingest/sensor via HTTP or MQTT
• Reads every 5–15 min; median filter applied before packaging
• JSON fields: node_id, timestamp, rain_mm, water_level_m, soil_moist_pct
Weather Ingestor
• Scheduler polls OpenWeatherMap / NOAA API → normalize forecast metrics
• Stores snapshot: wind_speed, gust, pressure, rain_1h, normalized_values
• Used by scoring engine as forecast_component input
Preprocessor
• Filters noise → computes deltas (e.g., water-level delta over last 30 min)
• Normalizes all values to 0–1 scale for the scoring engine
• Outlier rejection: flag readings deviating > 20% from moving median
AI / Decision Layer
• Rule-based module: immediate triggers on threshold breaches
• Decision Tree / Naive Bayes: trained on historical + simulated data
• Crowdsourced pipeline: image CNN returns severity + confidence → credibility score
Scoring Engine
• Weighted linear combination → Impact Score 0–100 → risk mapping (Low/Med/High)
• forecast_component + local_component + report_component × vulnerability_factor
• All weights configurable; intermediate values logged for explainability
Dispatcher & Dashboard
• Geofence mapping → target user list → FCM push or local notification
• Admin dashboard: simulate mode for demo (POST /admin/simulate_warning)
• App: map of sensors/reports/risks; forms for report submission and SOS
References: Huang et al. (Flood ML); Imran et al. (Crowdsourcing)

## Slide 7
7 — Technology Stack (Exact)
Hardware
• ESP32/ESP8266 dev boards
• Rain sensor module (YL-83/FC-37)
• Ultrasonic/pressure water-level sensor (JSN-SR04T)
• Soil moisture sensor (capacitive v1.2)
IoT Firmware
• Arduino (C++) or MicroPython for ESP32
• HTTP POST (JSON) or MQTT (Mosquitto)
• Median filter + sanity checks on-device
• Retry buffer for offline periods
Backend Server
• Python Flask or Node.js Express (either OK)
• MongoDB (document store) or Firebase Realtime/Firestore
• Scheduler: APScheduler (Python) or node-cron
• REST API endpoints documented in section 10
AI & ML
• Python — scikit-learn (Decision Tree, Naive Bayes)
• TensorFlow/Keras (small CNN / transfer learning)
• Scoring engine: pure Python weighted formula
• Rule-based logic: configurable threshold dict
Frontend & Push
• React (web) or Flutter (mobile) for citizen app
• Leaflet / Google Maps for risk map
• Firebase Cloud Messaging (FCM) for push notifications
• Optional: Twilio for SMS fallback
Hosting & Tools
• Local server for demo OR free-tier cloud (Heroku/Railway)
• Git / GitHub for version control
• Jupyter Notebook for model training & evaluation
• VS Code + Arduino IDE / PlatformIO
References: Espressif ESP32 manual; TensorFlow/Keras docs

## Slide 8
8 & 9 — Hardware & BOM + Database Schema & Collections
Hardware BOM (per node)
Component
Model
Est. Cost
ESP32 dev board
DEVKIT v1 / WROOM-32
$4 – 6
Rain sensor
YL-83 / FC-37
$2
Water-level sensor
JSN-SR04T (waterproof)
$3 – 6
Soil moisture sensor
Capacitive v1.2
$2
Wires, breadboard, enclosure, power bank
—
$3 – 5
TOTAL per node
Buy 1–3 nodes + spares
$15 – 25
Database Schema & Collections
Sensors
node_id, timestamp (ISO), rain_mm, water_level_m, soil_moist_pct, raw_payload
WeatherSnapshots
timestamp, area_id, wind_speed, gust, pressure, rain_1h, normalized_values
Reports
report_id, user_id, timestamp, lat, lon, photo_url, text, image_severity, image_confidence, credibility_score
Scores
area_id, timestamp, impact_score (0–100), components {forecast, local, report}, vulnerability_factor
Alerts
alert_id, area_id, timestamp_sent, recipients_list, severity (Low/Med/High), payload
Users
user_id, last_lat, last_lon, notification_token, opt_in_flags
Design DB indexes: timestamp, area_id, node_id, and geo indexes on user locations for geofencing. | Ref: MongoDB geospatial docs.

## Slide 9
10 — API Contracts & Sample Payloads
POST
/ingest/sensor
Sent by ESP32 every 5–15 min via HTTP POST or MQTT
{
"node_id": "esp32-01",
"timestamp": "2026-03-14T10:02Z",
"rain_mm": 12.4,
"water_level_m": 1.45,
"soil_moist_pct": 78
}
POST
/ingest/report
Submitted from citizen mobile/web app with photo upload
{
"report_id": "rep-001",
"user_id": "u-123",
"timestamp": "2026-03-14T10:03Z",
"lat": 6.9271, "lon": 79.8612,
"photo_url": "https://...",
"text": "road submerged"
}
GET
/score/area/{area_id}
Returns latest impact_score and component breakdown for dashboard
Returns:
{
"impact_score": 54,
"risk_level": "MEDIUM",
"components": { "forecast": 0.33,
"local": 0.18, "report": 0.09 }
}
POST
/admin/simulate_warning
For demo only: injects synthetic weather + sensor data to trigger scoring
{
"area_id": "ward-12",
"override_wind": 0.8,
"override_rain": 0.9,
"override_sensor_delta": 0.7
}
Document expected fields, units, and required authentication for admin endpoints. | Ref: OpenWeatherMap docs.

## Slide 10
12 — Impact Scoring Formula (Math + Worked Example)
Input Variables (all normalized 0–1)
Rf
Forecast rainfall
Wf
Forecast wind
Pt
Pressure drop trend
Sr
Recent sensor rainfall
Sw
Water level delta
Ss
Soil moisture
Rc
Report credibility
V
Vulnerability factor (0.2–1.0)
Weights
w_rf=0.25 w_wf=0.20 w_pt=0.10 w_sr=0.20 w_sw=0.15 w_rc=0.10
forecast_component = w_rf·Rf + w_wf·Wf + w_pt·Pt
local_component = w_sr·Sr + w_sw·Sw
report_component = w_rc·Rc
raw = forecast + local + report
impact_score = min(100, int(raw × 100 × V))
Risk Mapping
0–39 → Low
40–69 → Medium
70–100 → High
Worked Example
Inputs:
Rf=0.8, Wf=0.5, Pt=0.3, Sr=0.6, Sw=0.4, Rc=0.9, V=0.9
forecast_component:
0.25×0.8 + 0.20×0.5 + 0.10×0.3 = 0.2 + 0.1 + 0.03 = 0.33
local_component:
0.20×0.6 + 0.15×0.4 = 0.12 + 0.06 = 0.18
report_component:
0.10×0.9 = 0.09
raw:
0.33 + 0.18 + 0.09 = 0.60
impact_score:
int(0.60 × 100 × 0.9) = int(54) → 54
Risk level:
54 → MEDIUM RISK ⚠
Keep weights configurable; show intermediate values in logs for explainability. | Ref: NOAA impact-based guidance.

## Slide 11
13 — Geofencing & Targeting + Alert Content & UX
Geofencing Implementation
Partition region
Into polygons (wards/tiles) or rectangular grid (1 km²). Each polygon has a vulnerability_factor (0.2–1.0) based on historical risk.
Map users to polygon
Via user's last GPS location. Only alert users whose polygon's impact score >= threshold.
Severity routing
HIGH → immediate polygon only | MEDIUM → polygon + 1 buffer ring | LOW → advisory to district admin.
Tools
shapely (Python) or turf.js (Node) for point-in-polygon. MongoDB geo indexes for fast querying.
Alert Content & UX
🔴 FLOOD ALERT — HIGH
Body: Move to shelter X. Avoid road Y. Data: Impact Score: 78/100 | rain: 12.4mm | water: 1.45m Time: 2026-03-14T10:03Z
I'm safe
Request help
Delivery Channels
Primary:
FCM push (app must register notification token)
Fallback:
In-app message on next open; optional SMS via Twilio (paid)
Design rule:
Concise, local language if possible, one-line action oriented
Ref: Crisis communication best practices; GIS basics for geofencing.

## Slide 12
14 — Demo Plan (Step-by-Step Script)
Goal: Show complete end-to-end system in ~6 minutes
1
All
Start Backend & Dashboard
Start backend server. Open dashboard. Confirm server shows empty latest values → proves clean start.
2
M1
Live ESP32 Node
Turn on ESP32 or run sensor emulator. Show live sensor stream (rain_mm, water_level_m, soil_moist_pct) arriving and updating on dashboard in real time.
3
M3
Citizen Report with Photo
Trigger test report from mobile app: upload photo → image model estimates severity → credibility score displayed on dashboard. Show report appearing in authority queue.
4
M4
Simulate Weather Advisory
Use POST /admin/simulate_warning to inject synthetic weather data (high wind + heavy rain). Triggers scoring engine to recalculate impact score upward.
5
M2 & M4
Scoring & Classification
Show scoring engine: intermediate values (forecast, local, report components) + final impact_score rising in logs. Dashboard shows risk level upgrading: LOW → MEDIUM → HIGH.
6
M4
Geofenced Alert Delivered
Targeted push notification received on sample device. Alert appears on dashboard with action button. Show that only users in affected polygon receive alert.
7
M2
Confusion Matrix & Logs
Show M2's comparison: rule-based vs Decision Tree outputs side by side with confusion matrix. Show evaluation logs proving false positive rate. Conclude demo.

## Slide 13
15 — Implementation Plan & Timeline (10 Weeks)
Week 1
Project Setup
Project plan · Buy sensors · Repo & folder structure setup · Choose exact stack (Flask vs Node, Firebase vs MongoDB)
Wk 2–3
IoT Node + Server Ingest (M1)
M1: ESP32 hardware assembly · firmware development · sensor calibration
Basic server ingest endpoints ready: POST /ingest/sensor, POST /ingest/report
Wk 4–5
Risk Classifier + Report UI (M2, M3)
M2: Rule module + Decision Tree training on historical/simulated data
M3: Basic report endpoints & UI scaffolding
Week 6
Image CNN + Weather Ingest (M3, M4)
M3: Image model training & integration with credibility fusion
M4: Weather ingest normalization from OpenWeatherMap API
Week 7
Scoring + Geofencing + Alerts (M4)
M4: Scoring engine implementation + geofencing logic + FCM alert dispatch
Integrate scoring output with dispatcher
Week 8
Integration Testing (All)
Full data flow integration tests · Fix cross-component data format issues
End-to-end test: sensor → server → score → alert
Week 9
Evaluation & Metrics (All)
Run evaluation: confusion matrices · latency measurements · false positive rates
Compute all metrics; finalize figures for report
Wk 10
Demo Prep + Report (All)
Demo script rehearsal · Record backup demo video
Finalize slides · Submit final report (Ch1–Ch6 + Appendix)
⚠ Prioritize end-to-end minimal features first (one node → live alert) then layer in extras. If time is tight, drop SMS and image model training — keep rule-based + demo.

## Slide 14
16 — Testing, Evaluation & Metrics
Functional Tests
Ingest path
node → server → DB
✓ Measure latency & packet success rate
Report path
app upload → image classifier → dashboard
✓ Image correctly classified; appears with credibility score
Alert path
score computed → dispatch → push received
✓ Alert delivered within 60 seconds of trigger
Evaluation Metrics
Accuracy
Decision Tree vs rule-based for L/M/H risk classification (confusion matrix)
False Positive Rate
Number of alerts not corroborated by sensors. Target: minimize.
Alert Latency
Time from ingest to notify. Target: < 60 seconds for local event.
Coverage
Percent of affected users who received the alert.
Report Corroboration
Percent of crowdsourced reports verified by nearby sensor readings.
Collect logs and produce short tables & plots for the final report.

## Slide 15
17 & 18 — Risk Assessment & Mitigations + Budget & Procurement
Risk Assessment & Mitigations
⚠ Sensor hardware failure
→ Keep spare sensors; prepare synthetic data generator for demo fallback
⚠ Weather API downtime
→ Cache last forecast snapshot; support simulated warnings via /admin endpoint
⚠ False alarms
→ Require corroboration (sensor + report OR 2 sensors) for HIGH alerts; tune thresholds
⚠ User privacy concerns
→ Opt-in location sharing only; anonymize data in logs and DB
⚠ Time shortage
→ Prioritize end-to-end minimal features first; postpone SMS and image model refinement
Budget & Procurement
Item
Estimate
Per IoT node (hardware)
$15 – 25
Buy 1–3 nodes + spare sensors
$35 – 75
Cloud & push (Firebase free tier)
$0
Optional SMS (Twilio)
Paid – optional
Google Colab credits (model training)
~$5
Printing & documentation
~LKR 3,500
Transport for field testing
~LKR 3,000
Budget justification: low-cost nodes demonstrating the concept — not a production system. All software tools (Python, scikit-learn, TensorFlow, Flask, MongoDB) are free & open-source. SLIIT lab facilities cover hardware testing at no extra cost.

## Slide 16
19 & 20 — Limitations & Assumptions + Future Improvements
Limitations & Assumptions
Prototype-level
Limited number of nodes and coverage area — NOT a production national deployment
Scoring accuracy
Depends on available weather forecast quality (external API); quality varies by region
ML model generalization
Trained on limited historical/simulated data — may not generalize without more real data
Connectivity
Assumes sufficient mobile connectivity during demo to reach a critical mass of users
Cyclone scope
Only assesses impact of cyclone conditions on ground sensors — does NOT predict cyclone tracks
Future Improvements Roadmap
F1
LoRaWAN Integration
Deploy multiple distributed IoT nodes with LoRaWAN for larger coverage without Wi-Fi dependency
F2
Better ML Models
Improve models with more training data; explore lightweight ensemble methods and online learning
F3
Government Feeds
Integrate official DMC government feeds and real-time shelter capacity updates
F4
Offline & SMS
Add SMS fallback, offline data collection mode, and automatic rescue dispatch integration
F5
Community Features
Add community reporting incentives (gamification), multi-language support, and audio alerts

## Slide 17
21 & 23 — Deliverables Checklist + Viva / Exam Q&A Cheatsheet
Deliverables & Submission Checklist
✅
Filled Topic Assessment Form (signed) — use the exact doc R26-IT-146
✅
Code repository link: hardware firmware + backend + ML models + frontend
✅
Hardware photos, wiring diagrams, BOM for each node
✅
Demo video (2–4 minutes) showing end-to-end scenario
✅
Final report (Ch1–Ch6) with appendix — follow doc sections & wording
✅
Presentation slides & backup demo (pre-recorded)
Viva Q&A Cheatsheet
Q: How does the scoring work?
A: Weighted linear combination of normalized forecast + local sensor metrics + report credibility, multiplied by vulnerability factor — transparent and logged.
Q: How do you avoid false alarms?
A: Require corroboration: HIGH alert needs sensor + report OR 2 independent sensor nodes. Tune thresholds. Log intermediate values for audit.
Q: Why not use deep forecasting models?
A: Undergrad constraints: explainability, limited time, and limited training data. Rule-based + Decision Tree is pragmatic, defensible, and sufficient for this scope.
Q: What if sensors disagree?
A: Use majority logic and credibility scoring. Prefer corroborated reports. Notify admins when sensors disagree for manual review.
Q: What is the system's novelty?
A: No existing system combines low-cost multi-hazard IoT sensing + explainable AI scoring + crowdsourced image validation + geofenced alerts in one integrated platform.

## Slide 18
Disaster Monitoring & Emergency Response System
Gantt Chart & Work Breakdown Structure
Task
Who
W1
W2
W3
W4
W5
W6
W7
W8
W9
W10
1. Planning & Setup
All
2. IoT Node (M1)
M1
3. Server Ingest
All
4. Risk Classifier (M2)
M2
5. Report App (M3)
M3
6. Weather+Alerts (M4)
M4
7. Integration Tests
All
8. Evaluation & Report
All
Work Breakdown Structure — Key Deliverables per Member
M1
IT22557506
ESP32 node + firmware
Wiring diagram + BOM
Calibration report
Live sensor demo
M2
IT22272386
Classifier code
Confusion matrix
GET /risk/area/{id}
Rule vs DT report
M3
IT22638168
Citizen UI screens
CNN model + notebook
Credibility logic
Photo→dashboard demo
M4
IT22284716
Weather ingestor
Scoring engine
Geofence + FCM dispatch
Admin simulate + demo

## Slide 19
11 — Member-wise Responsibilities & Deliverables
M1
IT22557506
IoT Sensor Network & Data Acquisition
Responsibilities:
• Build ESP32 node (wiring, code, enclosure)
• Read sensors and sample at configured interval (5–15 min)
• Implement reliable data transmission (HTTP/MQTT) and retry logic
• Basic on-device preprocessing (median filter, sanity checks)
Deliverables:
✔ Hardware photos, wiring diagrams, BOM
✔ Firmware source code (GitHub)
✔ Live demo of node sending data to server
Why important: Provides ground-truth real-time data needed by ALL other modules.
M2
IT22272386
Flood & Landslide Risk Classification
Responsibilities:
• Define rule thresholds and windows (e.g., rainfall in last 30 min > X)
• Implement Decision Tree classifier trained on historical + synthetic data
• Provide API returning risk level for area/time
• Evaluate rule-based vs ML outputs and produce confusion matrix
Deliverables:
✔ Code for classifier, training scripts, evaluation plots
✔ Endpoint GET /risk/area/{id}
✔ Short comparison report: rule-based vs Decision Tree
Why important: Produces explainable risk classification used in dispatcher & dashboard.
M3
IT22638168
Crowdsourced Reporting & Image Validation
Responsibilities:
• Build mobile/web UI for report uploads and SOS
• Implement image preprocessing and CNN or transfer learning for water severity
• Provide credibility fusion logic (image_confidence + sensor corroboration)
• Rank reports by urgency and credibility score
Deliverables:
✔ UI screens, server endpoints, model code
✔ Demo: report reaches dashboard with credibility score
✔ Code for image classifier
Why important: Adds ground confirmation and reduces false positives.
M4
IT22284716
Cyclone Impact Evaluation & Alert Prioritization
Responsibilities:
• Integrate weather API; normalize forecast metrics
• Implement weighted scoring engine and vulnerability mapping
• Implement geofencing and alert dispatch via FCM
• Provide admin simulate mode for demo
Deliverables:
✔ Weather ingestor code, scoring module, dispatch module
✔ Dashboard panel showing impact scores and alert log
✔ Demo script: simulated advisory → targeted alert sent
Why important: Turns forecasts + sensors into actionable, localized emergency alerts.

## Slide 21
Conclusion
01
Real problem.
Sri Lanka faces recurring, preventable disaster casualties driven by delayed situational awareness. The gap is local, real-time environmental data.
02
Our solution.
Low-cost ESP32 IoT nodes + explainable AI scoring + citizen crowdsourcing + geofenced alerts — one integrated, end-to-end platform.
03
Team structure.
Each of the 4 members owns one critical layer. Together they form a complete pipeline: sense → process → classify → alert.
04
Practical & defensible.
We use simple, explainable models — not deep learning. Rule-based + Decision Tree is reliable, auditable, and justified for this scope and data availability.
05
What comes next.
LoRaWAN expansion, more training data, government feed integration, and community incentives for wider deployment across Sri Lanka.
Thank you — We welcome your questions.
Project R26-IT-146 | IT22557506 · IT22272386 · IT22638168 · IT22284716 | SLIIT — March 2026